## Slide 1: A Method to Implement Low Energy Read Operations, and Single Cycle Write after Read in Subthreshold SRAMs
Arijit Banerjee
Dated: 12/10/2012
VLSI
6332 Project

## Slide 2: Why did We Moved to Subthreshold Supply Voltages?
Reducing Ceff is Costly in terms of design effort
For Low frequency(in KHz) Medical Circuits, Vdd scaling to Subthreshold Voltages is Very Effective

## Slide 3: Problems in 6T based Subthreshold Bitcells
For 6T based 8T, 9T 10T … Half select Problem in Subthreshold domain
  Read Stress SNM in Half Selected Cells while Writing
  No Column Muxing a must
  Writeback (Two Cycle Write after Read ) a must in Writing

## Slide 4: How to lower Energy in 6T based Subthreshold SRAMs?
Possibly Voltage Scaling?
  Operating in Subthreshold Domain
  Voltage Scaling further? Not a good Idea!
  Vmin is Limited by Worst case RSNM, HSNM, VDRV, and so on

## Slide 5: Minimum Operation Voltage (Vmin) Dependency
Worse case μ - 3σ Read SNM(RSNM or RNM) for 6T
Worst Case
IBM 130nm data provided by James Boley BSN Chip Group @ UVa

## Slide 6: Vmin Dependency
Worse case μ - 3σ Hold SNM(HSNM) for 6T based 10T
Worst Case
MIT 180xlp data provided by James Boley BSN Chip Group @ UVa

## Slide 7: Vmin Dependency
Worse case μ + 3σ Data Retention Voltage (VDRV)
Worst Case
IBM 130nm data provided by James Boley BSN Chip Group @ UVa

## Slide 8: Possible Solutions to “How to lower Energy in 6T based SRAMs”
New Type of Bitcells
Novel Read/Write Methods
New SRAM Architectures

## Slide 9: Earlier Works in SRAM Dynamic Energy/Power Mitigation

## Slide 10: Can We do Better?
Using RAS-CAS DRAM Timing Concept in SRAM
Low Energy Read (LER)?
  Do Not operate Decoders, WL Drivers
“N-1” LER Operations per one Read in N word Row
Auto detection of LER

## Slide 11: Single Cycle Write after Read(WAR)?
Earlier Approach was Two Cycle Write after Read
Current Approach is Single Cycle Write after Read
  Pulsed Read and Write Word Line Generation in WAR
  Controllable WAR Margins through External Pins
  Using Intermediate Latch to Latch the Read Row Before Write

## Slide 12: Block Diagram of the 4KB Subthreshold Data Memory
128 Bit to 16 Bit Bus Interface Logic
Global Bitline Mux/Demux
Memory Array 4 Banks X 1 KB
Precharge and column Circuitry
128 Bit Intermediate Latch
Row and Bank Decoders
Column Decoders
Address Input Flops
Write after Read Control, Timing Control, LER Support Logic, and Power Control Logic
16 bit I/O Bus
11 Bit Address Bus
Control Signals

## Slide 13: 4KB Subthreshold SRAM Layout
Decoders and Word Line Drivers
Write after Read Control, Timing Control, LER Support Logic, and Power Control Logic
1KB Bank 1
1KB Bank 2
1KB Bank 3
1KB Bank 4
128 Bit to 16 Bit Bus Mux
Address Bus, Data Input Bus Control Signals
Data Output Bus

## Slide 14: What about Half Select Problem?
We do not solve it; We bypass it
No Column Mux used for avoiding half select problem
Gains? Penalty?

## Slide 15: Energy Comparison: Read vs. LER
Chart: Comparison of Read Energy @ 0.3V 27C with LER Energy @ 0. 5V 27C in 4KB Subthreshold Memory
LER Energy @ 0.5V 27C TT | 2.4727e-13
Read Energy @ 0.3V 27C TT | 7.3921e-13
LER Enrgy @ 0.5 27C FF | 2.8649e-13
Read Energy @ 0.3v 27C FF | 7.3133e-13
3X
Savings
2.5X Savings

## Slide 16: Subthreshold LER Energy Savings Trend with this Scheme
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 4KB Subthreshold SRAM
| 0.3 | 0.35 | 0.4 | 0.45 | 0.5
TT | 9.5949 | 6.4126 | 4.5935 | 7.4935 | 7.0085
FF | 2.2929 | 5.5362 | 3.5572 | 5.3138 | 6.4597
SS | 2.8151 | 5.117 | 6.0926
FS | 1.6743 | 6.8129 | 7.3541
SF | 4.8797 | 4.5251 | 5.9856 | 5.7227
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 4KB Subthreshold SRAM
| 0.4 | 0.45 | 0.5
TT | 4.5935 | 7.4935 | 7.0085
FF | 3.5572 | 5.3138 | 6.4597
SS | 2.8151 | 5.117 | 6.0926
FS | 1.6743 | 6.8129 | 7.3541
SF | 4.5251 | 5.9856 | 5.7227

## Slide 17: Above Subthreshold LER Energy Savings Trend
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 2KB High Speed SRAM
| 0.9 | 1 | 1.2
TT | 4.487 | 4.6325 | 4.7292
FF | 7.4179 | 8.3134 | 9.8035
SS | 4.7733 | 4.9624 | 5.0975
FS | 5.2473 | 5.4182 | 5.5606
SF | 4.214 | 4.3222 | 4.4908
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 2KB High Speed SRAM
| 0.9 | 1 | 1.2
TT | 4.487 | 4.6325 | 4.7292
FF | 7.4179 | 8.3134 | 9.8035
SS | 4.7733 | 4.9624 | 5.0975
FS | 5.2473 | 5.4182 | 5.5606
SF | 4.214 | 4.3222 | 4.4908

## Slide 18: How is LER Energy vs. Cycle Time?
Chart: LER Energy vs. Cycle Time @ 27C in 4KB Subthreshold Memory
| 2.1123499343960001E-5 | 6.5095485255119999E-6 | 2.0319119727529998E-6 | 6.8538369741020003E-7 | 2.3011199544780001E-7
TT | 4.684e-13 | 1.4644e-13 | 2.1295e-13 | 1.8062e-13 | 2.4727e-13
FF | 1.4025e-12 | 1.1675e-12 | 4.8545e-13 | 4.5472e-13 | 3.2704e-13
FS | 2.6436e-12 | 3.1026e-13 | 3.0613e-13
SF | 1.7534e-13 | 1.8332e-13 | 1.804e-13 | 2.3201e-13
SS | 3.7924e-13 | 2.2007e-13 | 2.4224e-13

## Slide 19: How is Read Energy vs. Cycle Time?
Chart: Read Energy vs. Cycle Time @ 27C in 4KB Subthreshold Memory
| 2.1123499343960001E-5 | 6.5095485255119999E-6 | 2.0319119727529998E-6 | 6.8538369741020003E-7 | 2.3011199544780001E-7
TT | 1.3742e-12 | 1.3627e-12 | 9.7818e-13 | 1.3535e-12 | 1.733e-12
FF | 2.9173e-12 | 2.876e-12 | 1.7269e-12 | 2.4163e-12 | 1.9521e-12
FS | 4.4262e-12 | 2.1137e-12 | 2.2134e-12
SF | 1.0262e-12 | 8.2956e-13 | 1.0798e-12 | 1.1982e-12
SS | 1.0676e-12 | 1.1261e-12 | 1.5166e-12

## Slide 20: How is Write after Read Energy vs. Cycle Time?
Chart: Write after Read Energy vs. Cycle Time @ 27C in 4KB Subthreshold Memory
| 2.1123499343960001E-5 | 6.5095485255119999E-6 | 2.0319119727529998E-6 | 6.8538369741020003E-7 | 2.3011199544780001E-7
TT | 4.4701e-13 | 5.4374e-13 | 5.3234e-13 | 1.0557e-12 | 1.4818e-12
FF | 2.5364e-12 | 2.2512e-12 | 7.8441e-13 | 1.0547e-12 | 1.4818e-12
FS | 1.7197e-12 | 9.0988e-13 | 1.5376e-12
SF | 2.638e-13 | 6.3038e-13 | 9.6927e-13 | 1.2874e-12
SS | 9.9161e-13 | 1.0804e-12 | 1.5756e-12

## Slide 21: Temperature Dependency of Cycle Time and Access Time
Chart: Temperature vs. Cycle Time in 4KB Subthreshold Memory @ 0.5V
| -40 | 0 | 27 | 65
TT | 1.2095e-06 | 3.8623e-07 | 2.3011e-07 | 1.3245e-07
FF | 1.808e-07 | 9.6473e-08 | 7.1395e-08 | 5.3763e-08
SS | 8.0099e-06 | 2.0502e-06 | 9.7029e-07 | 4.7159e-07
FS | 3.3011e-06 | 9.0298e-07 | 5.1202e-07 | 2.708e-07
SF | 2.2398e-06 | 4.3799e-07 | 2.4678e-07 | 1.3573e-07
Chart: Temperature vs. Access Time in 4KB Subthreshold Memory@ 0.5V
| -40 | 0 | 27 | 65
TT | 1.1473e-06 | 3.4933e-07 | 1.9778e-07 | 1.0555e-07
FF | 1.4993e-07 | 7.153e-08 | 4.9423e-08 | 3.8493e-08
SS | 7.8083e-06 | 1.9757e-06 | 9.1684e-07 | 4.3082e-07
FS | 3.2375e-06 | 8.6757e-07 | 4.8283e-07 | 2.4569e-07
SF | 2.1576e-06 | 3.8802e-07 | 2.0877e-07 | 1.0587e-07

## Slide 22: Comparison of Read Energy: Old vs. New Design

## Slide 23: Comparison of Write after Read (WAR) Energy: Old vs. New Design

## Slide 24: Comparison of Leakage Current: Old vs. New Design

## Slide 25: Comparison of Area and Cycle Time: Old vs. New Design

## Slide 26: Comparison With Prior Works

## Slide 27: Conclusion
7 LER Operations per one Read in 8 word Row
WAR Margins are Externally Controllable
Penalty of 7% area, 3% worst case Standby Leakage, 25% worst case WAR Energy, and 45% worst case Read Energy
Worst case 5.7X LER energy savings in KHz frequencies @ 0.5V 27C

## Slide 28: References
[1] J. P. Kulkarni, K. Kim, and K. Roy, “A 160 mV Robust Schmitt Trigger Based Subthreshold SRAM,” IEEE Journal of Solid-State Circuits, vol. 42, no. 10, pp. 2303–2313, Oct. 2007.
[2] I. J. Chang, J.-J. Kim, S. P. Park, and K. Roy, “A 32 kb 10T Sub-Threshold SRAM Array With Bit-Interleaving and Differential Read Scheme in 90 nm CMOS,” IEEE Journal of Solid-State Circuits, vol. 44, no. 2, pp. 650–658, Feb. 2009.
[3] T. H. Kim, J. Liu, J. Keane, and C. H. Kim, “A high-density subthreshold SRAM with data-independent bitline leakage and virtual ground replica scheme,” in Solid-State Circuits Conference, 2007. ISSCC 2007. Digest of Technical Papers. IEEE International, 2007, pp. 330–606.
[4] B. H. Calhoun and A. Chandrakasan, “A 256kb sub-threshold SRAM in 65nm CMOS,” in Solid-State Circuits Conference, 2006. ISSCC 2006. Digest of Technical Papers. IEEE International, 2006, pp. 2592–2601.
[5] G. K. Reddy, K. Jainwal, J. Singh, and S. P. Mohanty, “Process variation tolerant 9T SRAM bitcell design,” in Quality Electronic Design (ISQED), 2012 13th International Symposium on, 2012, pp. 493–497.
[6] Ali Valaee, Asim J. Al-Khalili, “SRAM Read-Assist Scheme for High Performance Low Power Applications” in International SoC Design Conference (ISOCC ) on , 2011, pp. 179-182.
[7] S. Yoshimoto, M. Terada, S. Okumura, T. Suzuki, S. Miyano, H. Kqwaguchi and M. Yoshimoto, “A 40-nm 0.5-V 20.1-µW/MHz 8T SRAM with Low-Energy Disturb Mitigation Scheme,” in IEEE Symposium on VLSI Circuits Digest of Technical Papers on, 2011, pp. 72-73.
[8] Atsushi Kawasumi, Toshikazu Suzuki, Shinich Moriwaki and Shinji Miyano, “ Energy Efficiency Degradation Caused by Random Variation in Low-Voltage SRAM and 26% Energy Reduction by Bitline Amplitude Limiting (BAL) Scheme,” in IEEE Asian Solid-State Circuits Conference on, 2011, pp. 165-168.
[9] Mohammad Sharifkhani, Manoj Sachdev, “A Low Power SRAM Architecture Based on Segmented Virtual Grounding,” in International symposium on Low Power Electronics and Design (ISLPED) on, 2006, pp. 256-261.
[10] A. Kawasumi, Y. Takeyama, O. Hirabayashi, K. Kushida, F. Tachibana. Y. Niki, S. Sasaki and T. Yabe, “Energy Efficiency Deterioration by Variability in SRAM and Circuit Techniques for Energy Saving without Voltage Reduction,” in IC Design & Technology (ICICDT), 2012 IEEE International Conference on, 2012.
[11] Mohammed Shareef I, Pradeep Nair, Bharadwaj Amrutur, “Energy Reduction in SRAM using Dynamic Voltage and Frequency Management,” in 2008 21st International Conference on VLSI Design on, 2008, pp. 503-508.
[12] http://download.micron.com/pdf/datasheets/psram/8mb_asyncpage_p23z.pdf
[13] http://www.issi.com/pdf/41C-LV16256C.pdf
[14] http://www.chiplus.com/Uploads/DataSheet/Pseudo%20SRAM/Pseudo_CS26LV32163%20(2.7).pdf

## Slide 29: Acknowledgements
Grad Students @ BSN Chip Team: James Boley , Yousef Shakhsheer, Alicia Klinefelter, Yanqing Zhang, Kyle Craig
Mateja Putic, Grad Student, UVa
Gary Lee, SEAS IT Administrator
Professor Mircea Stan, ECE, UVa
Professor Ben Calhoun, ECE, UVa

## Slide 30: Thank You! Questions?